## Slide 1: Forced oscillator
4th September 2018

## Slide 2: Review : The driven, undamped harmonic oscillator
The equation of motion for harmonically driven, undamped oscillator may be written as
If a general displacement x is given as , the amplitude A is found to be
depending on  = 0 or 
and 0 = frequency of free oscillation
The phase shift of “0” indicates that the displacement and the driving force are in phase.
The phase shift of “” indicated that the displacement and the driving force are out of phase by .
Notes: Phase  in the assumption of the displacement indicates that, in general, the displacement and driving force may be out of phase.

## Slide 3
(a) the amplitude of a driven oscillator versus  with no damping.
(b) The phase lag of the displacement relative to the driving force versus .
F0/s
Notes: As we throw in a little damping at  close to 0 the amplitude becomes large but finite. The phase shift smooth out; it is no longer discontinuous, although the shift is still quite abrupt.

## Slide 4: Behavior of forced oscillator
Consider a mechanical forced oscillator with force F0cost applied to damped oscillator.
The equation of motion is given by
The complete solution for the case is composed of
(1) Transient term and (2) Steady state term
time
displacement
Transient + steady state
steady state
http://www.acs.psu.edu/drussell/Demos/SHO/mass-force.html
Applied force
Displacement
Notes: In the plot the forcing frequency is f=0.4, so that the first oscillator is being driven below resonance. The grey curve shows the applied force (positive is upwards), and the purple curve shows the displacement of the mass in response to the applied force. After the transient motion decays and the oscillator settles into steady state motion, the displacement is in phase with force. Notice that the frequency of the steady state motion of the mass is the driving (forcing) frequency, not the natural frequency of the mass-spring system.

## Slide 5: Driven, damped harmonic oscillator
Generally, the applied force may be written as F0exp(it).
Therefore, the equation of motion becomes
Suppose a general solution of the differential equation is
By substituting the general solution into the equation of motion, we obtain the amplitude A as follows

## Slide 6: Description of the steady state term
Therefore, the displacement can be written as

## Slide 7: Complete information of magnitude and phase of the steady state term
The phase difference  between x
and F due to the reactive part
(m – s/m) of Zm.
(2) Extra phase difference gives x lags
F by 900 even  = 0.
The amplitude of the x is F0/Zm
1
2
3

## Slide 8: The amplitude of the x
Recall the maximum amplitude from the steady state,
The expression clearly states that the amplitude is a function of the driving frequency.
The amplitude is still finite even though the driving frequency is equal to the frequency of the free oscillation.
https://xmdemo.wordpress.com/2014/06/22/040-damping-and-resonance-amplitude/
What is the resonant frequency of the forced oscillator?
Notes: Resonant frequency w = wo^2 – r^2/2m^2
Remember that the frequency of the damping constant w’ = wo^2 – r^3/4m^2
Express the resonant frequency w in terms of damping frequency w’ : w^2 = w’^2 – r^2/4m^2

## Slide 9: A note on the applied force
Instead of using an exponential form, the applied force as written in terms of cosine or since functions leads to the steady state solution as follows
The value of displacement x resulting from F0cos(t) is
The value of displacement x resulting from F0sin(t) is
Both solutions satisfy the information given in the previous page.

## Slide 10: Mechanical Impedance Zm
Mechanical impedance is a measure of how much a structure resists motion when subjected to a harmonic force. It relates forces with velocities acting on a mechanical system.
Mechanical impedance is a complex quantity given by
The real part, the mechanical resistance, is independent of frequency.
The dissipative forces are proportional to velocity.
The imaginary part, the mechanical reactance, varies with frequency, becoming zero at the resonant and infinite at the antiresonant frequencies of the system.
https://en.wikipedia.org/wiki/Mechanical_impedance
Notes: From the summary above the imaginary part becomes zero when the frequency of the applied force is equal to the resonant frequency.
That is wm –s/w = 0 when w = (s/m)^1/2 which is the frequency of shm.
Anti resonant frequency makes the least amplitude of the oscillatory system.

## Slide 11: Relation of the velocity and force
The velocity is given by
In case of  = 0, velocity and force are in phase..
The amplitude of the velocity is F0/|Zm|, this leads to the definition of the mechanical impedance Zm = F/V

## Slide 12: Problem
The equation describes the motion of an undamped simple harmonic oscillator driven by a force of frequency . -Determine the steady state solution and sketch the behavior of the steady state amplitude versus .
-Also find the general solution.

## Slide 13: A response of RLC series circuit
The input voltage is equal the sum of the voltage across the inductor, the voltage across the capacitor and the voltage across the resistor.
If Va =V0exp(it) and q = q0exp(it), the solution of the above differential equation is given as
Where the electrical impedance Ze is written as
http://encyclopedia2.thefreedictionary.com/forced+oscillation
I
Va
Notes: the input voltage is equal to the sum of the voltage across the inductor, the voltage across the resistor, and the voltage across the capacitor, where the voltage across the inductor is the product of its inductance (L) and the rate of change of the current through the inductor; the voltage across the resistor is the product of its resistance (R) and the current passing through it; and the voltage across the capacitor is the integral over time of the current through the capacitor (that is, the charge on the capacitor plates) divided by the capacitance (C).
เมือเปรียบเทียบ phase ระหว่าง กระแสกับ driving voltage พบว่ามี เฟสตรงกัน

## Slide 14: Behavior of velocity v in magnitude versus driving for frequency 
The magnitude of the velocity amplitude varies with frequency  because |Zm| is frequency dependent.
The impedance is stiffness controlled : at low frequency, s/ dominates.
The impedance is mass controlled: at high frequency, m dominates.
Zero reactance or minimum impedance : Zm = r and velocity and driving force are in phase. This leads to the velocity resonance F0/r .
Velocity of forced oscillator versus driving frequency .

## Slide 15
According to the relationship between the velocity v and force F,
The applied force is
Generally, v lags F by  and
Consider 3 situations;  > 0,  < 0 and  = 0.
Phase behavior of velocity v versus driving force frequency 
http://www.analyzemath.com/trigonometry/properties.html
Notes: Don’t forget that the applied force is given as F = F0coswt.

## Slide 16
Variation of phase angle  versus
driving force frequency 
At low frequencies the velocity leads the force (  negative) and at high frequencies the velocity lags the force (  positive).

tan
/2
0
tan-
-/2
 = 0
tan = 0
 = 0
Mass controlled
Stiffness controlled
Notes: Don’t forget that the applied force is given as F = F0coswt.

## Slide 17: Behavior of displacement in magnitude versus driving force frequency 
Recall the displacement
Clearly, the amplitude is given as and
The amplitude function suggests that the graph of x vs  depends on 3 different ranges of .
What would the amplitude be when   0?
What would the amplitude be when    ?
What does the driving frequency give the amplitude resonance? (Next slide!)
Notes: The displacement here is a result of the driving force F = F0cost
What would x be when   0? The amplitude = F/s
What would x be when    ? The amplitude = F/mw^2  0

## Slide 18: The amplitude resonance of the displacement
The displacement resonance occurs when the denominator Zm is a minimum.
This takes place when
The condition gives the driving frequency  which gives the displacement resonance.
Therefore,
Thus, the displacement resonance occurs at a frequency slightly less than 0, the frequency of velocity resonance.
Express the driving resonance frequency in terms of damping frequency?
Notes: Note that if r is very small, the driving frequencies that gives displacement and velocity resonances are the same.
Express the driving resonance frequency in terms of damping frequency?
W^2 = w’^2 –r^2/4m^2

## Slide 19: Variation of the displacement of a forced oscillator vs driving force frequency 
The maximum displacement at resonance amplitude is given as
Due to (Prove this!)
Therefore,
The amplitude at resonance is kept low by increasing r.
Notes: By varying r to be either larger or lower, the amplitude resonance can be exploieted.
Keeping the resonance amplitude low is the principle of vibration insulation.
A negligible value of r produces a large amplification at resonance : this is the basis of high selectivity in a tuned radio circuit.

## Slide 20: Phase behavior of displacement versus driving force frequency 
Recall the displacement and the driving force
Since the displacement x lags velocity v by ..……………
Consider when   0, the above condition suggests that x lags/leads/is in phase with F.
Consider when   , x lags/leads/is in phase with F.
Consider when  = 0, x lags/leads/is in phase with F.
Notes: Note: x lags F by Pi at high frequency
X lags by Pi/2 at frequency of free oscillation w0

## Slide 21: Variation of total phase angle between displacement and driving force vs driving frequeny 

## Slide 22: Significance of the two components of the displacement curve (1)
From the displacement
This expression may be rewritten as
Due to and
The displacement is then composed of two terms: resistive fraction and reactive fraction,

## Slide 23: Significance of the two components of the displacement curve (2)
The amplitude of the reactive fraction may be written as
The amplitude of the resistive fraction may be written as
Resistive fraction
Reactive fraction

## Slide 24
This is clear that the reactive fraction becomes zero and resistive fraction is near its maximum at  = 0.
However, they combine to give a maximum at , the resonant frequency for amplitude displace, where
Significance of the two components of the displacement curve (3)

## Slide 25: Power supplied to oscillator by the driving force
To maintain the steady state, the average power supplied by the driving force just equals that being dissipated by the frictional force.
Average power supplied by the driving force
Dissipated power by frictional force
Notes: The instantaneous power P supplied is equal to the product of the instantaneous driving
force and the instantaneous velocity;

## Slide 26: Variation of Pav with ; Absorption resonance curve
The maximum average power is achieved when cos = 1 and Zm = r.
This corresponds to the case when  = 0 and velocity is in phase with applied force.
The sharpness of the peak at resonance is determined by the value of damping constant r.
The curve is known as the absorption curve of the oscillator

## Slide 27: The Q-value in terms of the resonance absorption bandwidth
The absorption curve in the previous slide can be used to defined the Q-value as follows
where 1 and 2 are frequencies at which the power supplied
And

## Slide 28: The Q-Value as an amplification factor
Note that for high values of Q, the damping constant r is small.
The displacement amplitude curve can be shown in terms of the quality factor Q of the system.

## Slide 29: Vibration isolation

## Slide 30: Vibration isolation
Generally, the vibration isolation can be divided into to two basic types ; i.e.,
(1) displacement isolation and (2) force isolation.
The moving-base model on the left is used in designing isolation to protect the device from motion of its point of attachment (base).
The model on the right is used to protect the point of attachment (ground) from vibration of the mass.
http://slideplayer.com/slide/8032841/

## Slide 31: Problem on displacement vibration insulation
y = vertical displacement of the base about its rest position.
x = vertical vibration of the floor about its equilibrium position
Requirement :Protect sensitive objects (i.e. heavy base) from vibrating floors and foundations.
Target : The ratio y/A is kept to a minimum.
Notes: The idea is simple: Protect sensitive objects from vibrating floors and foundations. So is the basic vibration-isolation system model,
The spring resists the movement of the vibration because it exerts an opposing force proportional to its displacement.
The damper consists of a piston moving through a viscous fluid, or a conductor moving in a magnetic field, and it removes kinetic energy and dissipate it as heat.

## Slide 32
Equation of motion
Suppose y > x;
Suppose
Determine the derivatives of y and x and substitute in the equation of motion.
This ends up in terms of the magnitude ratio as follows,
Problem on displacement vibration insulation (cont.)
Notes: y-x เป็นระยะกระจัดสัมพัทธ์ ของตัวถ่ายทอดการสั่นซึ่งประกอบด้วย sprint และ damper
dy/dt – dx/dt เป็นความเร็วสัมพัทธ์ของตัวถ่ายทอดการสั่น

## Slide 33: Physical meaning of the ratio |y/A|
What does it mean if the magnitude ratio is greater than 1?
Under the condition, this is found that or
Notes: Isolation is the reduction in transmitted vibration through the storage and controlled release of vibrational energy.
The figure shows the effect of adding damping to a spring mass system. In many cases, it is impossible to add enough damping to reduce peak transmitted vibrations to acceptable levels. Therefore, the system engineer must ensure that the natural frequency of the system is sufficiently below the disturbing frequency so the transmitted vibrations are minimized.

## Slide 34: Displacement Transmissibility |y/A|
The displacement vibration isolator will generally operate at the mass controlled end of the frequency spectrum and the resonant frequency is designed to be lower than the range of frequencies likely to be met.
http://machinedesign.com/archive/shaking-vibration-models
Notes: Isolation is the reduction in transmitted vibration through the storage and controlled release of vibrational energy.
The figure shows the effect of adding damping to a spring mass system. In many cases, it is impossible to add enough damping to reduce peak transmitted vibrations to acceptable levels. Therefore, the system engineer must ensure that the natural frequency of the system is sufficiently below the disturbing frequency so the transmitted vibrations are minimized.
 คือ damping ratio หรือ อัตราส่วนระหว่าง damping constant ของ system กับ critical damping constant ของระบบนั้น

## Slide 35: Analysis of the displacement transmissibility
From the displacement transmissibility the object vibrates less than the supporting surface of vibrating frequency if vibration frequency (region of isolation).
Lower-stiffness vibration isolators decrease the natural frequency 0 and transmit less vibration to the object for almost driving frequencies.
The increasing isolator damping reduces an object’s vibration amplitude at by lessens isolation at (region of amplification).
http://www.novibration.com/isoselectguide.htm
Notes: Because 0 ^2 = s/m, s then 0 

## Slide 36: Animation of displacement vibration isolator
https://www.thorlabs.com/tutorials/tables5.cfm

## Slide 37: Displacement transmissibility in terms of damping ratio 
By definition, the damping ratio  is given as the ratio of the damping factor to the critical damping factor,
This leads to
Therefore, the transmissibility in terms of  is written as
Notes: Transmissibility is another concept that summarizes particular behaviors of a mass, spring, damper system. It is the steady state amplitude ratio of output to input for a given frequency ratioand damping ratio.

## Slide 38: Problem : Effect of speed on the amplitude of car vibration
Given
(1) car speed = 20 km/hr
(2) car mass = 1007 kg
(3) stiffness s = 4 x 104 N/m
(4) damping constant r = 2000 Ns/m
Determine the amplitude response of the car to the vibrating road surface by considering the surface disturbance in the form of a sinusoidal input.
http://www.slideshare.net/SondiponAdhikari/base-excitation-of-dynamic-systems
y(t)
s
r
20 km/hr
Notes: Damping constant ค่าคงตัวของการหน่วง

## Slide 40: Force vibration isolation
The vibration source is mounted on isolator composed of a spring with stiffness s and a damper with damping constant r .
The mass is disturbed by a force F(t).
What is the force transmissibility for isolating the source of vibration?
http://slideplayer.com/slide/8032841/
s
r

## Slide 41
Equation of motion of mass m is given by
The solution as the displacement is written as
This can be written in terms of ,  and 0 as
Force vibration isolation (cont.)

## Slide 42
The response of the supporting base is due to the force combination of spring with stiffness s and damper with damping constant r .
By substituting x from the previous slide and determine the force transmissibility,
Force vibration isolation (cont.)
A = vibrating amplitude of the base

## Slide 43: Force transmissibility curve
http://www.kaztechnologies.com/faq/
Notes: What is transmissibility?
Transmissibility is another concept that summarizes particular behaviors of a mass, spring, damper system. It is the steady state amplitude ratio of output to input for a given frequency ratioand damping ratio. This amplitude ratio can be expressed in whatever units are of interest and most often will used as a measure of force transmitted or displacement transmitted. Transmissibility is a key concept to vibration isolation. One example of using this concept with respect to force is evaluating how a vibrating piece of equipment transmits force to the structure of a building and how this can be manipulated and reduced. A second example that would be concerned with transmitted displacement would be isolating sensitive equipment from a vibrating environment. Both of these concepts can also be extended to cars and race cars. The transmissibility plot below shows how amplitude ratio behaves as a function of frequency ratio for variousdamping ratios