## Slide 1: Vehicular accidents
19th August 2020

## Slide 2: Outline
Analytical tools
Case studies of car accidents
  Case study 1 : non collision
  Case study 2 : midnight crash

## Slide 3: Unit conversion
Multiply by |  |  | 
Convert from | Convert to |  | 
 | m/s | km/h | mph
m/s | 1 | 3.6 | 2.24
km/h | 0.278 | 1 | 0.62
mph | 0.45 | 1.609 | 1
http://www.engineeringtoolbox.com/velocity-units-converter-d_1035.html
Notes: For example convert from km/h to m/s by multiplied by 0.278
Convert m/s to km/h multiplied by 3.6

## Slide 4: Analytical tools
Analytical tools are used to evaluate the accidents.
The analysis provide the accident reconstruction scenario.
The analytical tools include
Kinematics
Work – kinetic energy theorem
Laws of conversation of momentum
Laws of conversation of energy

## Slide 5: Basic energy method
To bring a moving vehicle with a constant speed to a stop, a work by braking, skidding or crushing has to be done to reduce the vehicle’s kinetic energy to zero.
Skidding is a common way that causes the dissipation of kinetic energy of a vehicle.
The skid mark with some other information can be used to compute a speed of a vehicle.
http://www.bsharp.org/physics/skidmarks

## Slide 6: Features of skid marks
A skid mark is the mark made by a tire which is stopped rolling and slides on the road surface.
Different inflation of tires will lead to different appearances of the skid marks.
http://forum.e46fanatics.com/showthread.php?t=461865
Conventional marks are generally solid continuous streaks. They often begin and end abruptly. Skid marks from ABS on the other hand may follow an intermittent light and dark pattern.
https://www.quora.com/

## Slide 7: Features of skid marks
Different inflation of tyres will lead to different appearances of the skid marks.
Try to finish the matching game below and give reasons for your choices.
https://www.edb.gov.hk › 5_Lesson_7_worksheets_withAns
Notes: Under-inflated tyre-
contact of tyre edges with road > (firmer than) contact of centre part of tyre with road
 The depreciation of the edges of tyre is much faster;
 When sliding on road, it gives skid marks with missing centre part.
Over-inflated tyre-
contact of centre part of tyre with road > (firmer than) contact of tyre edges with road
causing skid marks with missing tyre edges

## Slide 8: Accident reconstruction
Case study 1 : non collision
An investigation of a single vehicle run-off case จาก In-depth Study on Road Accidents: Thailand Perspective
By
M B Islam, S Ponboon and N Boontob
Thailand Accident Research Center (TARC)
ศูนย์วิจัยอุบัติแห่งประเทศไทย (http://www.tarc.or.th/)
Asian Institute of Technology (AIT)
THAILAND

## Slide 9: แหล่งข้อมูล
http://www.tarc.ait.ac.th/th/index.php

## Slide 10: ข้อมูลเบื้องต้น
เหตุเกิดบนถนนพหลโยธินขาเข้ากรุงเทพฯ ในช่องทางด่วน
ขณะที่รถกระบะกำลังวิ่งด้วยความเร็วค่าหนึ่ง ยางหน้าด้านซ้ายแตก ทำให้รถเสียหลักพุ่งลงท้องร่องที่คั่นระหว่างช่องทางด่วนกับทางคู่ขนาน
ไม่มีผู้ได้รับบาดเจ็บในอุบัติเหตุครั้งนี้
Notes: The crash involved vehicle, Isuzu D-max, was reported to have front left tire blown out and running into the ditch on the left of the road on Highway No.1, Paholyothin. The driver, only one occupant, received no injury.

## Slide 11: รายละเอียดจากสถานที่เกิดเหตุ (1)
ถนนพหลโยธิน :
  บริเวณที่เกิดอุบัติเหตุเป็นเส้นทางตรง
  ผิวถนนแห้งและมีวัสดุผิวหน้าเป็น asphalt
ทางคู่ขนาน
ถนนพหลโยธิน
ท้องร่อง
เข้ากรุงเทพฯ
รอยไถล

## Slide 12: รายละเอียดจากสถานที่เกิดเหตุ (2)
รอยไถล หรือ skid marks บนไหล่ทางที่มีพื้นผิวเป็น asphalt
รอยไถลบริเวณถัดจากไหล่ทางซึ่งเป็นพื้นหญ้าและโคลน
รอยไถลบริเวณท้องร่องซึ่งพื้นผิวประกอบด้วยหญ้า โคลนและก้อนกรวด
ถนน พหลโยธิน
ท้องร่อง
พื้นหญ้า
ทางคู่ขนาน
To BKK
จุดที่รถหยุด
asphalt

## Slide 13: ข้อมูลสำหรับการวิเคราะห์เหตุการณ์ที่เกิดขึ้น
ระยะทางของรอยไถล บริเวณต่าง ๆ
  บริเวณไหล่ทาง  24 m
  บริเวณพื้นหญ้า  6 m
  บริเวณท้องร่อง  28 m
สัมประสิทธิ์ความเสียดทาน
(coefficient of friction) บริเวณต่าง ๆ
  บริเวณไหล่ทาง  0.84
  บริเวณพื้นหญ้า  0.64
  บริเวณท้องร่อง  0.62
Notes: Coefficient of friction ในที่นี้ควรเป็น dynamic friction (kinetic friction) ซึ่งมีค่าน้อยกว่าของ static friction

## Slide 14
Coefficients of friction used for different surface types
file:///C:/Users/RatchapakC/Downloads/CASRPotentialeffectsESC1114.pdf
(Kinetic friction)
A standard value for kinetic friction is 0.7
Notes: What is a sealed road?
A sealed road is one which has been formed using surface treatments such as tar, bitumen, concrete or asphalt. Therefore it has been permanently “sealed” using these materials.
Commonly, most Australian roads in major cities and surrounding suburbs are sealed.
What is an unsealed road?
An unsealed road is a road that has been formed and constructed but is not sealed with a hard material such as those mentioned above.

## Slide 15: ความสัมพันธ์ระหว่างงานและพลังงานจลน์
รอยไถลบอกความเร็วรถยนต์
ในขณะที่ล้อรถล็อกเนื่องจากการเบรก จะเกิดแรงเสียดทานจากพื้นถนนต้านการไถลของล้อ ทำให้บริเวณผิวหน้ายางเกิดความร้อนและละลายเกิดเป็นรอยไถลขึ้น พร้อมกันนี้ความเร็วของรถยนต์ลดลงหรือพลังงานจลน์น้อยลง ซึ่งเขียนออกมาในรูปของสมการได้เป็น
w = K = Kf – Ki 

## Slide 16
67 km/h (19 m/s)
75 km/h (21 m/s)
104 km/h (29 m/s)
Notes: #3 location v = 18.59 m/s (67 km/h)
#2 location v = 20.51 m/s (74 km/h)
#3 location v = 28.56 m/s (103 km/h)

## Slide 17: ข้อสังเกตเกี่ยวกับการเกิดรอยไถลบนพื้นถนนเนื่องจากการเบรก
http://www.tarorigin.com/art/Elivesay/
ในขณะที่คนขับเริ่มกดเบรก ล้อรถไม่ได้ถูกล็อกทันที เนื่องจากมีช่วงระยะเวลาในการตอบสนองและประสิทธิภาพการทำงานของระบบเบรก ดังนั้นค่าความเร็วที่ได้จากการคำนวณโดยอาศัยรอยไถล จึงเป็นค่าความเร็วที่น้อยกว่าค่าที่ควรจะเป็น

## Slide 18: กราฟ ระหว่างความเร็ว และ ระยะทาง ของรถกระบะที่ประสบอุบัติเหตุ

## Slide 19: อัตราความเร็วของยานพาหนะตามพระราชบัญญัติจราจรทางบก ฉบับ 8 พ.ศ. 2551
1.สำหรับรถบรรทุกที่มีน้ำหนักรถรวมทั้งน้ำหนักบรรทุกเกิน 1,200 กิโลกรัมหรือรถบรรทุกคนโดยสาร ให้ขับในเขตกรุงเทพมหานคร เขตเมืองพัทยา หรือเขตเทศบาลไม่เกิน 60 กิโลเมตรต่อชั่วโมง หรือนอกเขตดังกล่าวให้ขับไม่เกิน 80 กิโลเมตรต่อชั่วโมง
2.สำหรับรถยนต์อื่นนอกจากรถที่ระบุไว้ใน 1 ขณะที่ลากจูงรถพ่วงรถยนต์บรรทุกที่มีน้ำหนักรถรวมทั้งน้ำหนักบรรทุกเกิน 1,200 กิโลกรัม หรือรถยนต์สามล้อให้ขับในเขตกรุงเทพมหานคร เขตเมืองพัทยา หรือเขตเทศบาล ไม่เกิน 45 กิโลเมตรต่อชั่วโมง หรือนอกเขตดังกล่าวให้ขับไม่เกิน 60 กิโลเมตรต่อชั่วโมง
3.สำหรับรถยนต์อื่นนอกจากรถที่ระบุไว้ใน 1 หรือ 2 หรือรถจักรยานยนต์ ให้ขับในเขตกรุงเทพมหานคร เขตเมืองพัทยา หรือเขตเทศบาล ไม่เกิน 80 กิโลเมตรต่อชั่วโมง หรือนอกเขตดังกล่าวให้ขับไม่เกิน 90 กิโลเมตรต่อชั่วโมง
http://www.tarc.ait.ac.th/th/speed7.php

## Slide 20: Stopping distance
http://www.bstreetsmart.org/Road-Safety/Stopping-Distances/
ในแผนภาพนี้ reaction time มีค่าประมาณเท่าใด?
Notes: According to this chart the reaction time is found to be about 1 s.
However, a typical reaction for a driver is 1.5 s.
One reason for this increased risk is reaction time - the time it takes for a driver to realize a danger and reacting to it. Reaction time is critical and so if a driver is a little distracted then it will take them longer to react - which increases the time it takes them to brake.
Braking distance is the distance a car travels before stopping when the brakes are applied. The braking distance is affected by a variety of factors - the surface of the road - wet or dry, sealed or dirt, the quality of the tyres of the vehicle.

## Slide 21
Stopping distance
The stopping distance is found by adding the applicable perception-reaction (or thinking) distance and the applicable skid mark (or braking) distance.
Stopping distance = thinking distance + braking distance
Total braking distance (m) =
Thinking distance (m) =
Therefore, the stopping distance of the truck (m) =
58 m
44 m
102 m

## Slide 22: ผลสรุปจากการศึกษา
คณะผู้วิจัยจาก TARC สรุปปัจจัยที่มีผลต่อการเกิดอุบัติในครั้งนี้ว่าขึ้นกับ
  Vehicle factor : เนื่องจากสภาพของยางที่เก่า ขาดการดูแล มีแนวโน้มที่จะทำให้เกิดอุบัติเหตุได้ง่าย
  Human factor : เนื่องจากการขับรถเร็วเกินกว่าความเร็วที่กำหนด ทำให้ไม่สามารถบังคับรถได้เมื่อเกิดอุบัติเหตุ
  Road-environment factor : เนื่องจากไหล่ทางมีความลาดเอียงมาก ดังนั้นเมื่อรถเสียหลักพุ่งลงมาที่ไหล่ทาง การบังคับรถให้กลับมายังเส้นทางเดิมจึงเป็นไปได้ยาก

## Slide 23
Case study 2 : midnight crash
The case involves a lady driver (Carol) driving a red car which knocked down a young male pedestrian (Henry) around midnight at a road junction. The driver was not injured and passed the alcohol test. However, the pedestrian was hurt badly. The following sketch was drawn by your colleague 1 hour after the accident:
https://www.edb.gov.hk › 5_Lesson_7_worksheets_withAns

## Slide 24
-mass of the car and Carol: 1100 kg
-mass of Henry: 60 kg
-speed limit at the location: 50 km/h
- Friction coefficient = 0.7
-point of impact: 28 m from the nearby traffic lamps
-17 m long skid marks from the point of impact
-Henry lay on the ground
-clothes fibers and some blood spatters were found near Henry’s body
-a few street lamps were out of order during the accident
-the manufacturer of Carol’s car claimed that the maximum
acceleration of the car is 2.4 ms-2
Information provided for reconstruction

## Slide 25
Carol (the driver)
When I was hurrying to the hospital for work that night, I stopped my car before the red traffic light. The road was dark. After the traffic light turned green and making sure that the road ahead was clear, I drove across the road junction. Suddenly, I saw a person wearing dark clothes appearing in front of me. I swear that I couldn’t see him until the last moment. I pressed my horn sharply but he didn’t seem to have any response. Everything was too late and my car knocked him down. I applied the brake immediately to stop my car. I was so scared that I stayed in my car until the police came.
Testimony
Henry (the injured person)
After drinking with my friends, I left the bar around midnight. I intended to catch the last bus home. The pedestrian lamp was green and flashing when I was running across the road. Suddenly, without sounding its horn a car at high speed came to me from my right hand side and knocked me unconscious.

## Slide 26: What is your verdict? Who is lying?
To stop a moving car by accident, a driver has to respond to an obstacle ahead and then applying a brake to stop the car.
Generally, the stopping distance is composed of thinking distance and braking distance.
In this incident, the skid mark and some other information provided the car speed when hitting the pedestrian to be 15 m/s or 55 km/h. This actually was over the allowed speed limit in that area.
If the driver was on alert. Her thinking distance was found to be 23 m. The distance was too close to where she claimed to stop. She had to be lying!